## Slide 1: SMART INDIA HACKATHON 2026
TITLE PAGE
Problem Statement ID – 26172
Problem Statement Title – Low Latency and Efficient Voice Activator for Edge Devices
Theme – Smart Automation
PS Category – Hardware
Team ID – [Team ID]
Team Name – [Team Name]

## Slide 2: Hey Vayro: Edge Wake Word, Cloud ASR
[Team Name]
Proposed Solution (Describe your Idea/Solution/Prototype)
Detailed explanation of the proposed solution
ESP32-S3 + INMP441 microphone listen continuously; every 10 ms the chip computes a 40-band log-mel frame
A 10.7 k-parameter DS-CNN (28 KB int8, TensorFlow Lite Micro + ESP-NN) scores the last 1 s every 60 ms
“Hey Vayro” detected (mean of 3 scores ≥ 0.70) → 571 ms pre-roll + live audio stream over one warm TCP link
Server: VAD ends the utterance, Vosk (Kaldi) ASR returns the command text
How it addresses the problem
No audio leaves the device until the keyword is detected → privacy, zero cloud cost while idle
Inside the PS budget on real hardware: 245.6 KiB peak RAM, 4.7 % idle CPU
Low latency: first audio at the server ≈ 2 ms after detection; keyword end → server ≈ 95 ms
Only open-source components; custom keyword trained from scratch (no pre-trained wake word)
Innovation and uniqueness of the solution
Training and device share one bit-exact feature pipeline (12 000 / 12 000 frames identical)
Pre-roll ring buffer: a command spoken with no pause after the keyword is never clipped
Learns from real homes: its own logged false triggers become hard negatives (model v4)
Each model is chosen by a rule written before testing; 58 logged evidence entries
28 KB
int8 model · 13.4 KB tensor arena
245.6 KiB
peak RAM while streaming (< 256 KB)
4.7 %
idle CPU, both cores (busiest core 8.8 %)
≈ 95 ms
keyword end → server (median)

## Slide 3: TECHNICAL APPROACH
[Team Name]
Technologies to be used (e.g. programming languages, frameworks, hardware)
Hardware: ESP32-S3 N16R8 (240 MHz, PSRAM off) + INMP441 I2S MEMS mic
Firmware: C / C++ on ESP-IDF 5.5.5 (FreeRTOS)
TinyML: TensorFlow Lite Micro + ESP-NN kernels, TFLM microfrontend
Training: Python, TensorFlow / Keras, Piper TTS (4 voices), LibriSpeech, our own recordings
Server: Python TCP ingest, energy VAD, Vosk / Kaldi ASR
Verification: bit-exact host twin of the front end, scripted capture and replay tools
Methodology and process for implementation (Flow Charts/Images/ working prototype)
Runtime — on the ESP32-S3 until the keyword, then the server
Mic
I2S, 16 kHz, 24-bit
Front end
30/10 ms, 40 log-mel
DS-CNN
int8, 1 s window, every 60 ms
Decide
mean of 3 ≥ 0.70, 2 s refractory
Ring
0.75 s, 571 ms pre-roll
Wi-Fi TCP
40 ms packets, warm link
Server
VAD end-point → Vosk ASR
ESP32-S3 (edge)
network · server
How the keyword model is made (all scripted, reproducible)
Data
TTS “Hey Vayro”, speech, room & household audio
Device-identical streams
same front end, bit-exact twin
Train
DS-CNN from random init
int8 export
28 KB, 5 ops
Select
rule declared before the test
Flash
operating point ships with the model
Working prototype: ESP32-S3-N16R8 + INMP441 on a breadboard (SCK→GPIO6, WS→GPIO5, SD→GPIO4). The demo video shows keyword → stream → transcript live on this board.
Model: 10 665 parameters · 212 584 MACs per inference · 28 024 B int8 · tensor arena 13 404 B · ops: Conv2D, DepthwiseConv2D, FullyConnected, Reshape, Logistic

## Slide 4: FEASIBILITY AND VIABILITY
[Team Name]
Analysis of the feasibility of the idea — measured on the physical prototype, final firmware
Efficiency
245.6 KiB
peak RAM, streaming (< 256 KB)
4.7 %
idle CPU, 2 cores (max core 8.8 %)
28 KB
model flash · 13.4 KB arena
Accuracy (model v4)
21 / 25
held-out keyword prompts, 0.5–2 m
10 / 10
fresh keyword + command prompts
0 in 5 h
false triggers, quiet night (held-out)
Latency
1.7 ms
detection → first packet at server
≈ 95 ms
keyword end → server (median)
136 ms
keyword end → server (p95)
Potential challenges and risks
Strategies for overcoming these challenges
TV / family speech still triggers: 10.4 per hour (held-out household audio)
Hard negatives mined from the device’s own false triggers already cut 15.1 → 10.4 /h; next: more household hours, server-side second check that drops streams with no command
Real-voice testing so far: one main speaker (plus TTS voices in 4 accents)
Scripted 3-minute sessions for new speakers; per-speaker results reported separately
Server ASR word accuracy is set by the ASR model (Vosk en-in: 36 % WER published)
Edge is ASR-agnostic: swap in a larger model or a command grammar on the server only
Thin RAM margin; Wi-Fi or server outages
Memory trims saved 9.6 KB; detection keeps running offline; auto-reconnect; ASR off the server’s receive path

## Slide 5: IMPACT AND BENEFITS
[Team Name]
Potential impact on the target audience
ISRO labs & control rooms: hands-free voice commands where hands and eyes are busy — without streaming room audio all day
Smart automation: a ready wake-word front end for any ESP32-class home, office or factory device
Assistive use: voice control for elderly or motor-impaired users on low-cost hardware
Indian developers & start-ups: custom keyword with Indian-accent training data, no vendor SDK or licence fee
0 bytes
of audio sent until the keyword is detected
32 kB/s
16 kHz audio, only from keyword to end of command
Benefits of the solution (social, economic, environmental, etc.)
Social
Privacy by design: the room is only heard by the chip until someone says “Hey Vayro”
Economic
Hardware ≈ ₹1 000 (estimate); open-source stack; no cloud cost while listening
Environmental
Low compute (4.7 % CPU idle); audio is sent only after the keyword, so traffic stays tiny. Wi-Fi is kept awake for latency; power not yet measured
Technical
Reproducible: a new keyword = new recordings + the same scripts; every number traceable to an evidence log

## Slide 6: RESEARCH AND REFERENCES
[Team Name]
Details / Links of the reference and research work
[1] Y. Zhang, N. Suda, L. Lai, V. Chandra, “Hello Edge: Keyword Spotting on Microcontrollers”, arXiv:1711.07128, 2017 — DS-CNN architecture
[2] P. Warden, “Speech Commands: A Dataset for Limited-Vocabulary Speech Recognition”, arXiv:1804.03209, 2018 — KWS background (not used for training)
[3] TensorFlow Lite Micro + microfrontend: github.com/tensorflow/tflite-micro
[4] Espressif esp-tflite-micro and ESP-NN: github.com/espressif/esp-tflite-micro · github.com/espressif/esp-nn
[5] ESP-IDF v5.5 (FreeRTOS, drivers, lwIP): github.com/espressif/esp-idf
[6] V. Panayotov et al., “LibriSpeech: an ASR corpus based on public domain audio books”, ICASSP 2015 — openslr.org/12
[7] Piper TTS and voices: github.com/OHF-Voice/piper1-gpl · huggingface.co/rhasspy/piper-voices
[8] D. Povey et al., “The Kaldi Speech Recognition Toolkit”, ASRU 2011 · Vosk: alphacephei.com/vosk
[9] Datasheets: ESP32-S3 Technical Reference Manual (Espressif); INMP441 (TDK InvenSense)
Our own research record
Evidence ledger: 58 entries, each tagged measured / estimated / proposed, with its raw data
Selection rules: written and committed before each held-out test
SBOM: every component and licence listed; the one closed Wi-Fi radio blob and the non-commercial TTS voices are disclosed
Licence: our code Apache-2.0; every component’s licence listed in the SBOM
Demo video: link to be added